## Slide 1
Asteroid Mission Design
Weekly Progress Update
Multi-target trajectory screening, launch feasibility & L2 departure analysis
August 11, 2026

## Slide 2
What we built this week
From a single hand-tuned porkchop plot to an automated, multi-target screening pipeline
1
Corrected flyby targeting
Reconnaissance flybys now use real B-plane offset targeting instead of a disguised collision trajectory
2
Multi-asteroid batch screening
One script now screens N candidates at once for intercept, flyby, and rendezvous cost
3
10 real candidates acquired
Selected via JPL's NHATS list + Close-Approach Data tool; downloaded via a Horizons API script
4
Discovery-to-reachability check
Given each object's real discovery date, is it reachable by its next close-approach window?
5
LEO launch-window feasibility
Injection Δv and launch-site (inclination) reachability layered on top of the cheapest transfers
6
Sun-Earth L2 departure (Tier 1)
First-order comparison of staging through L2 vs. launching directly from LEO

## Slide 3
Three mission types, one Lambert solver
Restricted two-body, zero-revolution Lambert transfers, patched-conic at Earth
Intercept
Targets the asteroid's exact position at arrival. Minimizes launch C3 — the kinetic-impactor case.
Flyby
Targets a point offset from the asteroid by a chosen standoff (500 km) in the B-plane, so the pass is a real reconnaissance geometry, not a near-miss collision.
Rendezvous
Targets the exact position and burns to match the asteroid's velocity on arrival. Minimizes total mission Δv.

## Slide 4
10 candidates, selected deliberately
A mix of well-characterized flown-mission targets and low-Δv NHATS candidates, so the comparison has real spread
Target | Source | Why included
2024 YR4 | existing | Original working target; Dec 2028 Earth approach
99942 Apophis | CAD tool | Famous near-zero-cost natural approach, Apr 2029
101955 Bennu | flown mission | OSIRIS-REx sample-return target
162173 Ryugu | flown mission | Hayabusa2 target
25143 Itokawa | flown mission | Hayabusa (original) target
65803 Didymos | flown mission | DART target — deliberately the “hard” case
2011 AA37 / 2012 EC / 2013 WA44 / 2001 CQ36 | NHATS list | Low-Δv (~5–6 km/s round trip) small NEAs
Target
Source
Why included
Discovery dates and Earth close-approach dates pulled from JPL's SBDB and CAD APIs
10
candidates screened

## Slide 5
Screening results: launch cost varies 600×
Best-case launch characteristic energy (C3) for a direct intercept, by target
Chart: C3 [km²/s²]
| Apophis | Ryugu | 2024 YR4 | 2013 WA44 | Itokawa | 2001 CQ36 | 2011 AA37 | 2012 EC | Bennu | Didymos
Launch C3 (km²/s²) | 0.004 | 0.009 | 0.01 | 0.149 | 0.259 | 0.409 | 0.52 | 0.75 | 0.81 | 2.502

## Slide 6
How patient does each mission need to be?
Time of flight across all 10 candidates, at each mission type's own optimum
Intercept
100–355 days
range across the batch
Median
282 d
Mean
273 d
Flyby
105–740 days
range across the batch
Median
372 d
Mean
380 d
Rendezvous
105–495 days
range across the batch
Median
232 d
Mean
264 d

## Slide 7
Reachable soon after discovery?
Real discovery dates + real Earth close-approach dates define two windows: can a mission launch after discovery and arrive by the second close approach that follows it?
Discovery
1st approach
(period 1 ends)
2nd approach
(period 2 ends)
period 1
period 2 — the deadline checked here
Didymos: no close approach inside its downloaded ephemeris window — reported as unavailable, not guessed at.
9 / 9
evaluable candidates reachable
by their next period
(C3 ≤ 30 km²/s² threshold, adjustable)

## Slide 8
Cheapest ≠ launchable
Injection Δv from a 400 km / 28.5° LEO parking orbit, and whether each target's cheapest transfer is actually launchable without a plane-change burn
Why it matters
A departure trajectory's C3 fixes its speed, but not its direction. The departure asymptote's declination (DLA) must fall within the parking orbit's inclination, or the launch needs an extra plane-change burn.
That's a real geometric constraint, independent of how cheap the transfer looks on a porkchop plot.
5 / 10
targets' cheapest-C3 transfer is directly launchable from this parking orbit
Injection Δv across the batch: 3.18 – 3.29 km/s
For the other 5, the cheapest directly-launchable date costs only marginally more — not a large penalty here

## Slide 9
Sun-Earth L2 vs. direct LEO escape
Tier 1 approximation: L2 modeled as co-moving with Earth, offset ~1.5M km; +3.2 km/s fixed cost to stage there first
Chart: Total mission departure Δv [km/s]
| Ryugu | Apophis | 2024 YR4 | 2013 WA44 | 2001 CQ36 | Itokawa | 2011 AA37 | 2012 EC | Bennu | Didymos
Total via LEO (direct) | 3.177 | 3.177 | 3.177 | 3.183 | 3.195 | 3.188 | 3.2 | 3.211 | 3.214 | 3.291
Total via L2 | 3.421 | 3.457 | 3.551 | 3.311 | 3.635 | 3.967 | 3.716 | 3.823 | 4.013 | 4.519

## Slide 10
Where this leaves us
CONFIRMED THIS WEEK
Flyby analysis now uses genuine B-plane targeting
10-target batch screening pipeline runs end to end
9 of 9 evaluable targets reachable by next period
LEO launch-window feasibility layered onto cost
OPEN QUESTIONS / NEXT STEPS
L2 result (LEO cheaper for all 10) is Tier 1 only — blind to low-energy manifold departures
Tier 2 (real CR3BP halo-orbit dynamics) would need a standalone three-body solver
Generalize plot_porkchop.py beyond 2024 YR4 to any target file
Decide: worth building Tier 2, or is Tier 1 sufficient for our purposes?
All code, data, and full result tables available in the shared project folder.